## Slide 1: AFTER/CHIC experimental connections
Two different physics cases
with a common apparatus concept
AFTER@LHC : experimental constraints
CHIC@SPS : experimental design

## Slide 2: AFTER @ LHC – Physics
Idea : use LHC beam on fixed target
  7 TeV proton beam (s ~115 GeV)
    p+p, p+A
  2.75 TeV Pb beam (s ~72 GeV)
    Pb+A, Pb+p
High boost and luminosity giving access to
  QCD at large x
  nPDF and nuclear shadowing
  QGP
  Spin physics
  Other ?
See Stan’s talk

## Slide 3: AFTER @ LHC – Beam extraction
Beam extraction @ LHC
…
Nbeam ~ 5 x 108 p+/s
…

## Slide 4: AFTER @ LHC – p+A Luminosity
Intensity: expect 5.108 protons.s-1
  Beam: 2808 bunches of 1.15x1011 protons = 3.2x1014 protons
  Bunch: Each bunch passes IP at the rate: 3.105km.s-1/27 km ~ 11 kHz
  Instantaneous extraction: IP sees 2808 x 11000~3.107 bunches passing every second  extract 5.108/3.107 ~ extract 16 protons in each bunch at each pass
  Integrated extraction: Over a 10h run: extract 5.108p x 3600s.h-1 x 10h=1.8 1013p.run-1  extract 1.8 x 1013/(3.2 x 1014)~5.6% of the protons stored in the beam
Instantaneous Luminosity
  L = Nbeam x NTarget = Nbeam x (r x e x NA)/A
  Nbeam=5 x 108 p+/s
  e (target thickness) = 1 cm
Integrated luminosity
  9 months running/year
   1year ~ 107 s
   yearL = Linstx107
Targ | r (g.cm-3) | A | Linst (mb-1.s-1) | yearL (pb-1.y-1)
Liq H | 0.068 | 1 | 20 | 200
Liq D | 0.16 | 2 | 24 | 240
Be | 1.85 | 9 | 62 | 620
Cu | 8.96 | 64 | 42 | 420
W | 19.1 | 185 | 31 | 310
Pb | 11.35 | 207 | 16 | 160
1 cm thick target

## Slide 5: AFTER @ LHC – p+A Luminosity
Typical numbers
  J/Y @ s=115 GeV
    sY ~ 1.5 103 nb
   BrYe+e- dsY/dy(y=0) ~ 30 nb
   @ s=115 GeV
    Bre+e- ds /dy(y=0)@ 115 GeV ~ 50 pb
Target | r (g.cm-3) | A | L (mb-1.s-1) | L (pb-1.y-1) | NJ/Y¦y=0 (y-1) NJ/Y = ALsY | N¦y=0 (y-1) N = ALs
Liq H | 0.068 | 1 | 20 | 200 | 6 106 | 1. 105
Liq D | 0.16 | 2 | 24 | 240 | 1.4 107 | 2.4 105
Be | 1.85 | 9 | 62 | 620 | 1.6 108 | 2.8 105
Cu | 8.96 | 64 | 42 | 420 | 8.1 108 | 1.3 106
W | 19.1 | 185 | 31 | 310 | 1.7 109 | 2.9 106
Pb | 11.35 | 207 | 16 | 160 | 1. 109 | 1.7 106
With 1 cm thick target

## Slide 6: AFTER @ LHC – Pb+Pb Luminosity
Intensity: expect 7.105 Pb.s-1
Integrated luminosity
  1 month running/year
   1year ~ 106 s
   yearL = Linstx106
Typical numbers : PHENIX @ RHIC recorded in 2010
    Au+Au @ 200 GeV: 1.3 nb-1
    Au+Au @ 62 GeV: 0.11 nb-1

## Slide 7: AFTER @ LHC - Pseudorapidity
h* = h – yCMS
forward region: h*>0
backward region: h*<0
Very high boost:
  With 7 TeV beam : g = 61.1
  With 2.75 TeV beam: g = 38.3
Very well placed to access backward physics
Note : taking x2 = M/s e-y
      x2(J/Y) = 1  yJ/Y ~ -3.6
      X2() = 1  y ~ -2.4
7 TeV
2.75 TeV
h*=-4.5
h*=-4
h*=-4
h*=-3.5
h*=0
h*=0
yCMS= 4.8
yCMS= 4.3
h*=-4.8
h*=-4.3

## Slide 8: AFTER @ LHC – Multiplicity
Number of charged particles/rapidity unit
  (1.5 x ~ charged+neutral)
  p+p @ 115 GeV ~ 2
  d+Au @ 200 GeV: max~11
  Au+Au @ 62.4 GeV: max~450
PRL 93, 082301 (2004)
PRC 74, 021901(R) (2006)
p+p
d+Au

## Slide 9: AFTER @ LHC – Detector
Typical detector: -3.5 < ycms < 0
  Multipurpose detector:
    Vertex
    Tracking
    Calorimetry
    Muons
  Compact detector
    Because of the high boost, the detector must be as compact as possible
    Need ultra-granular technologies
EMcal
Hcal
MuID
~1 m
~0.1 m
~0.2 m
~1 m
~2 m
h*=0

## Slide 10: AFTER @ LHC – Detector
Dimension
Detector | Zmin/Zmax | Rmin/Rmax
Vertex | 40/50 cm | 0.5/35 cm
Tracker | 50/150 cm | 0.8/90 cm
EMCal | 150/170 cm | 2/100 cm
Hcal | 170/270 cm | 2.5/160 cm
muons | 270/470 cm | 4/300 cm
vertex
tracker
EMCal
HCal
muons
3 m
5 mm
~4.5 m

## Slide 11: AFTER @ LHC – Conclusion
Wide physics case
  QCD at large x
  nPDF and shadowing
  QGP
  Spin
  Other ?
Up to 7 TeV beam
  very high boost
  need ultra-granular (new) technologies
Connection with the CHIC experiment @ SPS
  Physics : QGP, nPDF and shadowing
  The CHIC @SPS experiment also needs ultra-granular technologies
  Take advantage of the CHIC expertise to design AFTER

## Slide 12: CHIC @ SPS – Physics case
Test charmonium sequential screening in a QGP
Measure cc in A+A @ 17 GeV
  How cc is suppressed relative to J/Y ? Dependence with y, pT, Npart,… ?
  Mandatory to draw the whole picture (SPS .vs. RHIC .vs. LHC)
  Goal: measure cc  J/Y g  m+m- g within ycms [-0.5, 0.5]
  Challenge: measure cc’s g in a high p0 multiplicity environment
Measure charmonia production in p+A
what is the depence of charmonia suppression with rapidity @SPS energies?
Crucial to understand effects due to cold nuclear matter
Goal : measure charmonia within ycms [-0.5, 2]
(See Tuesday talk)

## Slide 13: CHIC @ SPS – experimental setup
Active target  vertex  spectrometer  calorimeter  absorber  muID
Dipole field
Muon Filter
(absorber)
target
vertex
tracking
tracking
MuID
Beam
EMCal

## Slide 14: CHIC @ SPS – Tracking
The NA60 pixel detector
The CHIC pixel detector
~40 cm
~100 cm
L = 0.4 m
L = 1 m

## Slide 15: CHIC @ SPS – Calorimetry
Need very high segmentation
  Expect up to ~400 photons/rapidity unit
  Need to separate two electromagnetic showers
  Need to isolate photons from p+/- contamination
W + Si calorimeter à la Calice
  30 layers
  0.5 x 0.5 cm2 pads
  24 X0 in 20 cm
  DE/E ~ 20% / E
W+Si : two relevant quantities
  Distance between 2 incoming particles: at least one free pad
  Moliere Radius
Geometrical condition: in principle
Dg > 2cm
bad
good
Set detector position according to event multiplicity
at CHIC: zcalo ~ 2m

## Slide 16: CHIC @ SPS – Calorimetry
Full simulation performed with the Calice Ecal proto
<E>~3 GeV
Pb+Pb
3 photons with E~2 GeV
distance between each photon~ 2 cm
(full simu made by D. Jeans - Calice collab.)
0.5 x 0.5 cm² pads

## Slide 17: CHIC @ SPS – Absorber
m
p+
DHCal
http://newsline.linearcollider.org/archive/2010/20101104.html
Absorber type
  NA50/NA60 : measure muon momentum after the absorber
   must minimize multiple scattering
  Must use low Z material: best = BeO (but expensive)
  NA50 : 0.6 m BeO + 4 m C + 0.6 m Fe = 5.2 m
CHIC : measure muon momentum before the absorber
 minimization of multiple scattering not crucial
 can use Fe material To absorb p+/-
Need to match muon track position between spectrometer and trigger : Use an instrumented Fe absorber
Can match muon track momentum between spectrometer and trigger : Use magnetized Fe absorber ?
Minos

## Slide 18: CHIC @ SPS – Overall design
Primary goals :
    cc  J/Y + g  m+ m- g at yCMS = 0
    J/Ym+ m- in large yCMS range
Detector features : very compact
    Spectrometer
      - Measure tracks before absorber  sM~20 MeV/c²
      - Covers yCMS [-0.5, 2]  need high segmentation
       Silicon technologies
    Calorimeter
      - Measuring g in high p0 multiplicity environment
       ultra-granular EMCal (Calice)
    Absorber/trigger
      - Using 4.5 m thick Fe to absorb p/K and low P m+/-
      - Can use smaller absorber if Fe magnetized
      - Trigger to be defined (expected rate = 0.3 kHz)
Expected performances
    tracking :
    Calorimetry :
Dipole field

## Slide 19: CHIC @ SPS – Performances
cc2 in p+p collisions at s=17.8 GeV
  Sample:
    20 kevents with Pythia 6.421
    1 cc2J/Y g m+ m- g per event
    Smearing DPm/Pm = 1%
    Smearing DEg/Eg = 20%/Eg
  Selections :
    Keep muons w/ -0.5 < ycms < 0.5
    Keep muons w/ Pz > 7 GeV
    Keep muons w/ zvertex < 215 cm
    Keep photons w/ -0.5 < ycms < 0.5
    Reject photons w/ Mgg [100, 160] MeV/c²
  Results : signal/bkg = 2.8
cc2 in Pb+Pb at s=17.8 GeV
  Sample:
    10 kevents minbias with Epos 1.6
    1 pythia cc2 embedded in each event
    Same selections as in p+p
    Reject g if not in the same hemisphere as J/Y
  Results : signal/bkg = 3.6

## Slide 20: AFTER/CHIC - Conclusion
CHIC : (contact : F. Fleuret)
  Very strong physics case : measure cc in Pb+Pb collisions @ SPS energies
  not done in the 90’s-00’s because needed technologies not available at that time
  Today, ultra-granular technologies are mature
  Measuring cc in Pb+Pb collisions is now doable
  Contact: F. Fleuret (fleuret@in2p3.fr) – LLR, Elena Ferreiro – Santiago
AFTER :
  Wider physics case (QCD at large x, nPDF, nuclear shadowing, QGP, spin physics)
  Up to 7 TeV beam, very high boost, need ultra-granular technologies
  Take advantage of the CHIC expertise to design AFTER
  Contact: J.-P. Lansberg (lansberg@in2p3.fr) - IPNO, S. Brodsky – SLAC, F. Fleuret – LLR, C. Hadjidakis – IPNO
Timescale and plans :
  July 7th 2011 : one-day meeting
  October 2011 :
    Draft of a Letter Of Intent for CHIC to be submitted to SPS-C by the end of the year.
    GDR-QCD meeting.
  December 2011 : CHIC/AFTER ANR calls for proposal
    simulations for CHIC (experimental)/AFTER (physics)
  2012 : AFTER expression of interest